## Slide 1
COMPUTER NETWORKS · CHAPTER 6
The Data Link Layer
Turning a raw physical link into something that reliably delivers frames between two directly-connected nodes — one bit, one byte, one frame at a time.
A condensed, illustrated edition for lecture use

## Slide 2
01
Connecting Nodes
What a link is physically, and the hard ceiling on how fast it can carry data.
Part 1 — Connecting Nodes
Data Link Layer
2

## Slide 3
CONNECTING NODES
What a Link Actually Is
Part 1 — Connecting Nodes
Data Link Layer
3
Every practical link relies on electromagnetic radiation traveling through some medium — or through free space.
One way to characterize a link: which medium it uses.
Guided media
Copper wire — twisted pair, coaxial (DSL, cable)
Optical fiber — home fiber and most long-haul backbone links
Signal is confined to a physical conductor
Predictable path, easiest to shield from interference
Unguided media
Air / free space — radio, microwave, infrared
Signal radiates outward, shared by anyone nearby
No wire to tap — but no wire to hide behind, either
Shared "wire": must divide it by frequency and space

## Slide 4
CONNECTING NODES
Frequency, Wavelength, and Encoding
Part 1 — Connecting Nodes
Data Link Layer
4
Frequency — how fast the electromagnetic wave oscillates, measured in hertz (Hz).
Wavelength — the distance between successive peaks: wavelength = (speed of light) / frequency.
Modulation — varying a signal’s frequency, amplitude, or phase to carry information.
Encoding — the specific job of placing binary data onto a signal so the receiver can recover it.
wavelength = speed of light ÷ frequency
Every encoding scheme in the next section is really just a way of answering: how do we modulate a signal so 1s and 0s survive the trip?

## Slide 5
CONNECTING NODES
The Shannon–Hartley Capacity Bound
Part 1 — Connecting Nodes
Data Link Layer
5
However cleverly a link is engineered, its usable bandwidth and background noise set a hard ceiling on capacity — no encoding trick can cross it.
C = B × log₂(1 + S/N)
  B = bandwidth (Hz), S/N = signal-to-noise ratio
A classic voice-grade phone line:
bandwidth B = 3300 – 300 Hz = 3000 Hz
30 dB of noise → S/N = 1000
C = 3000 × log₂(1001) ≈ 30,000 bps
So how did 56-kbps modems exist? They pushed close to a
better bound at the phone company’s digital switch — not past this one.

## Slide 6
02
Encoding: Bits to Signal
Three attempts at turning a bitstream into a signal — each one fixing the last one’s flaw.
Part 2 — Encoding: Bits to Signal
Data Link Layer
6

## Slide 7
ENCODING
NRZ: The Obvious Encoding
Part 2 — Encoding: Bits to Signal
Data Link Layer
7
Non-Return-to-Zero: the simplest possible mapping — hold the signal high for a 1, low for a 0.
Bits flow between adaptors; signals flow between the physical components in between.
1
0
1
1
0
0
0
1
0
1
1
0
NRZ
Simple to generate — but two problems appear as soon as real bit patterns show up.

## Slide 8
ENCODING
NRZ's Two Problems
Part 2 — Encoding: Bits to Signal
Data Link Layer
8
Baseline wander
Receiver tracks a running average signal level to tell high from low.
A long run of the same bit drags that average toward it.
Eventually the signal and the "average" converge — 1 and 0 become indistinguishable.
Too many consecutive 0s or 1s confuse the receiver
Clock recovery
Sender and receiver are each driven by their own clock — one bit transmitted, one bit sampled, per tick.
Frequent transitions are what let the receiver’s clock resynchronize.
A long run with no transition lets the two clocks drift apart.
No transition ⇒ no chance to resynchronize
Both failure modes have the same root cause: long runs of identical bits.

## Slide 9
ENCODING
NRZI: A Transition Encodes a One
Part 2 — Encoding: Bits to Signal
Data Link Layer
9
Non-Return-to-Zero Inverted: to send a 1, transition to the opposite signal level; to send a 0, stay where you are.
A run of consecutive 1s now produces a steady stream of transitions — clock recovery is fixed for that case.
1
0
1
1
0
0
0
1
0
1
1
0
NRZI
Same bit sequence as before — notice the two adjacent 1s now toggle the line. A long run of 0s, though, still leaves it flat.

## Slide 10
ENCODING
Manchester Encoding: Merge Clock with Data
Part 2 — Encoding: Bits to Signal
Data Link Layer
10
Transmit the exclusive-OR of the NRZ-encoded data and an internal clock signal, so every bit carries its own transition.
0 = low→high transition; 1 = high→low transition (mid-bit)
1
0
1
1
0
0
0
1
0
1
1
0
Manchester
Every single bit cell has a transition in its middle — the receiver can resynchronize on every bit, no matter the data.

## Slide 11
ENCODING
The Cost — and a Summary
Part 2 — Encoding: Bits to Signal
Data Link Layer
11
Manchester doubles the rate at which the signal transitions on the link — the receiver has half the time to detect each pulse.
Baud rate = rate of signal transitions. Bit rate = rate of data. In Manchester, bit rate is half the baud rate.
Scheme
Rule
Fixes
Cost
NRZ
High = 1, low = 0
— (baseline)
Wander + clock drift
NRZI
Transition = 1, hold = 0
Runs of 1s
Runs of 0s remain
Manchester
XOR data with clock
Runs of 0s and 1s
2× transition rate

## Slide 12
03
Framing
Where does a frame start and end? Three families of answers.
Part 3 — Framing
Data Link Layer
12

## Slide 13
FRAMING
From Bitstream to Frames
Part 3 — Framing
Data Link Layer
13
Packet-switched networks exchange blocks of data — frames — not raw bitstreams. Bits flow between adaptors, frames flow between hosts.
The central challenge for the adaptor: recognize exactly which set of bits makes up one frame.
Byte-oriented
BISYNC, PPP
Special sentinel bytes mark the start and end of a frame.
Byte-counting
DDCMP
A length field states how many bytes the frame body holds.
Bit-oriented
HDLC
A bit pattern marks the boundary; stuffed bits keep it unique.

## Slide 14
FRAMING · BYTE-ORIENTED
Sentinel Framing: BISYNC and PPP
Part 3 — Framing
Data Link Layer
14
BISYNC (IBM, late 1960s) marks a frame with SYN, then brackets the data with STX … ETX sentinel characters.
PPP, common on Internet links today, uses a single flag byte 01111110 at both ends of the frame instead.
Either way: if the sentinel value appears inside the data, it must be escaped so the receiver isn’t fooled.
PPP FRAME FORMAT
Flag
Addr / Ctrl
Protocol
Payload
Checksum
Flag
01111110
default values
IP / IPX (16 bit)
negotiated, ≤ 1500 B
error detection
01111110

## Slide 15
FRAMING · BYTE-COUNTING
DDCMP: Count the Bytes
Part 3 — Framing
Data Link Layer
15
A Count field states how many bytes of data follow — the receiver simply reads that many bytes and stops.
Fragile: if the Count field itself is corrupted, framing is lost entirely.
The receiver has no way to know where the (wrong-length) frame really ends — it must resynchronize on the next recognizable header.
DDCMP FRAME FORMAT
SOH
Count
Header CRC
Data
Data CRC
start of header
bytes in body
checks header only
Count bytes
checks the body

## Slide 16
FRAMING · BIT-ORIENTED
HDLC: One Pattern, Bit Stuffing
Part 3 — Framing
Data Link Layer
16
HDLC brackets every frame with the same flag pattern used by PPP: 01111110 — at both start and end.
Rule: whenever five consecutive 1s appear in the frame body, the sender stuffs in an extra 0 before the next bit.
This guarantees the flag pattern can never occur by accident inside the payload.
Original data bits: 1 1 1 1 1 0 1 1 1 1 1 1 1 0
Five 1s in a row → stuff a 0 right after each run of five
Transmitted: 1 1 1 1 1
0 (stuffed)
0 1 1 1 1 1
0 (stuffed)
1 1 0

## Slide 17
FRAMING · BIT-ORIENTED
HDLC: Unstuffing on the Way In
Part 3 — Framing
Data Link Layer
17
The receiver watches for five consecutive 1s, then inspects the next bit to decide what it means.
After five 1s, next bit…
Meaning
Action
0
A stuffed bit
Discard it, keep receiving data
1, then 0 (01111110)
End-of-frame flag
Frame complete — deliver it
1, then 1 (01111111)
Error in the bitstream
Discard the whole frame; wait for the next flag

## Slide 18
FRAMING
Comparing the Three Families
Part 3 — Framing
Data Link Layer
18
Approach
Examples
Boundary marker
Weak point
Byte-oriented
BISYNC, PPP
Sentinel byte(s), escaped in data
Escaping adds overhead per occurrence
Byte-counting
DDCMP
A count field naming the body length
One corrupted count derails the whole stream
Bit-oriented
HDLC
Flag pattern 01111110, protected by bit stuffing
Stuffing/unstuffing costs extra bits and logic
Every approach is solving the same problem: mark a boundary unambiguously, without banning any possible data value.

## Slide 19
04
Error Detection
Redundant information lets the receiver notice when a frame has been damaged in transit.
Part 4 — Error Detection
Data Link Layer
19

## Slide 20
ERROR DETECTION
The Basic Idea
Part 4 — Error Detection
Data Link Layer
20
Electrical interference and thermal noise flip bits in transit — the receiver needs a way to notice.
Extreme (bad) idea: send two full copies of the frame.
  n bits of data cost n more bits of redundancy — expensive, and matching corruption still slips through.
Goal: strong protection from a little redundancy — k redundant bits with k ≪ n.
12,000
bits of data in a full-size Ethernet frame
32
bits of CRC protecting all of it
375×
data bits per redundant bit — and still very strong

## Slide 21
ERROR DETECTION
Two-Dimensional Parity
Part 4 — Error Detection
Data Link Layer
21
Ordinary (1-D) parity adds one bit per byte so the count of 1s is always even (or always odd).
Two-dimensional parity repeats the trick across bytes too: a parity bit per row, and a parity byte for the whole frame.
Byte
b1
b2
b3
b4
Row parity
A
1
0
1
1
1
B
0
1
1
0
0
C
1
1
0
0
0
D
0
0
0
1
1
Parity byte
0
0
0
0
0
(even parity: every row and every column sums to an even number of 1s)
Catches all 1-, 2-, and 3-bit errors, and most 4-bit errors — for a cost of roughly one extra bit per eight.

## Slide 22
ERROR DETECTION
The Internet Checksum
Part 4 — Error Detection
Data Link Layer
22
Treat the data as a sequence of 16-bit words; add them all up using ones-complement arithmetic; transmit the complement of the sum.
The receiver redoes the same sum over the received data and checksum together — a mismatch means something was corrupted.
Ones-complement arithmetic: a carry out of the top bit wraps around and is added back in.
Example (4-bit): add −5 and −3
+5 = 0101 → −5 = 1010 +3 = 0011 → −3 = 1100
1010
+ 1100
------
10110 ← carry out of the top bit
0110 + 1 (the carry) = 0111
0111 is the ones-complement of 1000 = −8, as expected.
Cheap to compute in software — but weak: it can’t catch every reordering or combination of flipped bits. Not used at the link level.

## Slide 23
ERROR DETECTION
CRC: The Strong Option
Part 4 — Error Detection
Data Link Layer
23
Treat the frame as one giant binary polynomial M(x). Sender and receiver both know a fixed generator polynomial C(x).
The CRC bits are chosen so the transmitted polynomial divides evenly by C(x), with remainder 0.
Message
M(x)
Append r zero bits
xʳ·M(x)
Divide by C(x)
remainder R(x)
Transmit
M(x) with R(x) attached
The receiver divides the received bits by the same C(x): remainder 0 means clean; nonzero means the frame was corrupted.
The only thing sender and receiver need to agree on in advance is C(x) itself.

## Slide 24
ERROR DETECTION
Why CRC Is Strong
Part 4 — Error Detection
Data Link Layer
24
A well-chosen generator polynomial C(x) is provably able to detect:
  All single-bit errors, if the xᵏ and x⁰ terms have nonzero coefficients.
  All double-bit errors, if C(x) has a factor with at least three terms.
  Any odd number of bit errors, if C(x) contains the factor (x + 1).
  Any burst error shorter than the CRC’s own degree — and most longer bursts too.
Standard generator polynomials:
CRC-8 = x8 + x2 + x + 1
CRC-16 = x16 + x15 + x2 + 1
CRC-CCITT = x16 + x12 + x5 + 1
CRC-32 = x32 + x26 + … + x2 + x + 1 ← used in Ethernet, HDLC, ZIP

## Slide 25
ERROR DETECTION
Choosing a Technique
Part 4 — Error Detection
Data Link Layer
25
Technique
Cost
Strength
Used in
2-D parity
Moderate (~1 bit / 8)
Catches most small clusters of errors
BISYNC
Internet checksum
Very cheap
Weak — misses some patterns entirely
IP, TCP, UDP headers
CRC
Cheap in hardware
Very strong, provable guarantees
Ethernet, HDLC, DDCMP, Wi-Fi
Detecting an error is only half the story — the other half is what to do once you’ve found one.

## Slide 26
05
Reliable Transmission: ARQ
Turning a link that occasionally loses or damages frames into one that delivers them reliably.
Part 5 — Reliable Transmission: ARQ
Data Link Layer
26

## Slide 27
RELIABLE TRANSMISSION
Acknowledgements and Timeouts
Part 5 — Reliable Transmission: ARQ
Data Link Layer
27
A corrupted frame gets caught by CRC and simply discarded — recovering from that loss is the link protocol’s job.
Acknowledgement (ACK)
  a small control frame the receiver sends back to confirm a frame arrived.
Timeout
  if no ACK shows up in a reasonable time, the sender retransmits the original frame.
This combination — Automatic Repeat reQuest (ARQ) — is the foundation every reliability scheme in this section builds on.

## Slide 28
RELIABLE TRANSMISSION
Stop-and-Wait
Part 5 — Reliable Transmission: ARQ
Data Link Layer
28
After sending one frame, the sender waits for its ACK before sending the next. A missing ACK triggers a timeout and a retransmission.
A 1-bit sequence number (0 / 1) lets the receiver tell a retransmission apart from the next new frame.
Frame and ACK both arrive
Sender
Receiver
Frame
ACK
ACK arrives before the timer expires — next frame goes out.
Frame is lost → timeout → retransmit
Sender
Receiver
frame lost
timeout
Frame (retransmit)
The receiver sees only one copy — the second attempt.

## Slide 29
RELIABLE TRANSMISSION
Stop-and-Wait's Throughput Problem
Part 5 — Reliable Transmission: ARQ
Data Link Layer
29
Only one frame is ever outstanding at a time — fine on a short, fast link, but wasteful once the bandwidth-delay product grows.
1.5 Mbps
link, 45 ms round-trip time
≈ 8 KB
bandwidth × delay — the pipe’s true capacity
≈ 182 Kbps
achieved with 1 KB frames — about 1/8 of capacity
To use the link fully, the sender needs up to eight frames in flight at once before waiting for an ACK — that’s the motivation for a sliding window.

## Slide 30
RELIABLE TRANSMISSION
Sliding Window: Keeping the Pipe Full
Part 5 — Reliable Transmission: ARQ
Data Link Layer
30
The sender may have up to SWS (send window size) frames outstanding at once, instead of just one.
0
1
2
3
4
5
6
7
8
9
10
11
SWS — outstanding (unacknowledged) frames allowed
LAR (last ACK received)
LFS (last frame sent)
Acknowledged
Sent, awaiting ACK
Not yet sent
Invariant kept by the sender:
  LFS − LAR ≤ SWS

## Slide 31
RELIABLE TRANSMISSION
Sender and Receiver Invariants
Part 5 — Reliable Transmission: ARQ
Data Link Layer
31
Sender
SWS — upper bound on outstanding frames
LAR — sequence number of the last ACK received
LFS — sequence number of the last frame sent
Buffers up to SWS frames, each with its own timer, in case a retransmit is needed
Invariant: LFS − LAR ≤ SWS
Receiver
RWS — upper bound on out-of-order frames it will accept
LFR — sequence number of the last frame received in order
LAF — sequence number of the largest acceptable frame
ACK is cumulative: it names the highest in-order frame seen, even if later frames already arrived
Invariant: LAF − LFR ≤ RWS
An out-of-window frame (SeqNum ≤ LFR or SeqNum > LAF) is simply discarded.

## Slide 32
RELIABLE TRANSMISSION
Sizing the Window, and Wrapping Around
Part 5 — Reliable Transmission: ARQ
Data Link Layer
32
Choosing SWS is easy — set it to roughly the bandwidth×delay product, so the pipe never runs dry.
RWS is a design choice: RWS = 1 needs no reorder buffer; RWS = SWS lets the receiver buffer out-of-order frames and keep the pipe fuller after a loss.
Sequence numbers are finite (e.g., 3 bits → 0–7) and must wrap around — which raises a subtle question.
If RWS = 1: SWS + 1 ≤ MaxSeqNum is enough.
If RWS = SWS: SWS + 1 is NOT enough — a lost ACK can make an old
frame’s retransmission look identical to a new one.
Safe rule when RWS = SWS: SWS < (MaxSeqNum + 1) / 2

## Slide 33
06
Ethernet
Carrier Sense, Multiple Access, Collision Detection — the protocol that has run the world’s LANs for 40 years.
Part 6 — Ethernet
Data Link Layer
33

## Slide 34
ETHERNET
Ethernet and CSMA/CD
Part 6 — Ethernet
Data Link Layer
34
Developed at Xerox PARC in the mid-1970s, building on the ALOHA packet-radio protocol; standardized with DEC and Intel as 10-Mbps Ethernet (1978), then IEEE 802.3.
CSMA/CD — Carrier Sense Multiple Access with Collision Detection
Carrier Sense
Every node can tell whether the shared link is idle or busy before it starts.
Multiple Access
One shared link; any node can send, and every node hears every transmission.
Collision Detection
A sender keeps listening while it transmits, so it can notice its frame colliding with another.

## Slide 35
ETHERNET
The Ethernet Frame Format
Part 6 — Ethernet
Data Link Layer
35
Implemented directly in hardware on the network adaptor — this is the frame every host on the segment sees.
Preamble
Dest. Addr
Src. Addr
Type
Data (payload)
CRC
64 bits
48 bits
48 bits
16 bits
46 – 1500 bytes
32 bits
Preamble — alternating 0s and 1s so the receiver can synchronize with the incoming signal.
Type — a demultiplexing key naming the higher-level protocol (e.g. IP).
Data must be at least 46 bytes — padded if the payload is shorter — so the frame is long enough to detect a collision (more on this shortly).

## Slide 36
ETHERNET
Ethernet Addressing
Part 6 — Ethernet
Data Link Layer
36
Every adaptor in the world has a unique 48-bit Ethernet address, usually burned into ROM — the address belongs to the adaptor, not the host.
Printed as six hex byte-pairs, e.g. 8:0:2b:e4:b1:2 — each manufacturer is assigned its own address prefix (AMD: 8:0:20…).
Unicast & broadcast
A unicast address names exactly one adaptor.
An address of all 1s is the broadcast address — every adaptor delivers it to its host.
Sent once, received everywhere on the segment
Multicast
First bit set to 1, but not the all-1s pattern.
A host programs its adaptor to accept a chosen set of multicast addresses.
Accepted: own address, broadcast, subscribed multicast

## Slide 37
ETHERNET
Access: Listen, Then Send
Part 6 — Ethernet
Data Link Layer
37
Line idle → transmit immediately.
Line busy → wait for it to go idle, then transmit immediately.
Ethernet is "1-persistent": whenever a busy line goes idle, a waiting adaptor transmits with probability 1.
No central control — so two (or more) adaptors can begin transmitting at the same instant. Their frames collide.

## Slide 38
ETHERNET
Collisions and Exponential Backoff
Part 6 — Ethernet
Data Link Layer
38
On detecting a collision, the sender finishes a 32-bit jamming sequence (so everyone else notices too), then stops.
It then waits a random amount of time before trying again — doubling the range of that random wait after each further collision.
After n collisions
Wait k × 51.2 µs, for random k in…
Example
1st collision
0 or 1
k ∈ {0, 1}
2nd collision
0 – 3
k ∈ {0, 1, 2, 3}
3rd collision
0 – 7
k ∈ {0, …, 7}
n-th collision
0 to 2ⁿ − 1
range doubles each time
This doubling strategy is exactly what gives the algorithm its name.

## Slide 39
ETHERNET
Why a Minimum Frame Size?
Part 6 — Ethernet
Data Link Layer
39
A sender must still be transmitting when word of a collision could get back to it — otherwise it will never know to retransmit.
Host A
Host B
t
t + d
t + 2d
A’s frame
B starts just before A arrives — collision at B
jam reaches A
A must keep transmitting until t + 2d to be guaranteed to see any possible collision — that sets a floor on frame size.

## Slide 40
ETHERNET
Frame Size and Cable Length Are Linked
Part 6 — Ethernet
Data Link Layer
40
For the worst case (the two most distant hosts on the segment) to always be caught, the round trip must fit inside the time it takes to send the smallest allowed frame.
51.2 µs
worst-case round-trip delay on a maximally sized Ethernet
512 bits
= 64 bytes: the minimum legal Ethernet frame
2500 m
maximum reach, with up to 4 repeaters between hosts
Shrink the minimum frame and you must shrink the maximum cable length to match — the two numbers are two sides of the same constraint.
In practice, most Ethernets are far shorter than 2500 m and run well under heavy load — this bound is rarely the limiting factor day to day.

## Slide 41
07
Wireless Networks: 802.11
A shared medium you can’t fully sense — collision avoidance takes the place of collision detection.
Part 7 — Wireless Networks: 802.11
Data Link Layer
41

## Slide 42
WIRELESS NETWORKS
Wireless Links Share the Air
Part 7 — Wireless Networks: 802.11
Data Link Layer
42
License-exempt bands need no license, but come with limits: capped transmit power (shorter range) and a requirement to use spread spectrum — spreading the signal over a wider band to reduce interference.
Base-station model
One fixed endpoint, wired to the Internet (the base station / access point).
The other endpoint is typically mobile.
Client-to-client traffic is routed through the base station.
Used by Wi-Fi, cellular networks
Ad-hoc / mesh model
No base station — nodes are peers.
A message may be relayed through a chain of intermediate peer nodes.
Topology can change as nodes move.
Self-organizing, no fixed infrastructure

## Slide 43
802.11 · COLLISION AVOIDANCE
The Hidden Node Problem
Part 7 — Wireless Networks: 802.11
Data Link Layer
43
A and C can each reach B, but not each other. If both send to B at once, their signals collide there — and neither sender can tell.
A
B
C
collide at B
A and C cannot hear each other — each is "hidden" from the other

## Slide 44
802.11 · COLLISION AVOIDANCE
The Exposed Node Problem
Part 7 — Wireless Networks: 802.11
Data Link Layer
44
B is sending to A. C hears B’s transmission and assumes it must stay silent — but C wants to send to D, which wouldn’t interfere with A at all.
A
B
C
D
B → A
C → D — perfectly safe
C hears B (they’re "exposed" to each other) but sitting silent here helps no one

## Slide 45
802.11 · COLLISION AVOIDANCE
MACA: Collision Avoidance via RTS/CTS
Part 7 — Wireless Networks: 802.11
Data Link Layer
45
Before sending data, the sender and receiver exchange short control frames — warning nearby nodes that a transmission is about to begin.
S
R
N
RTS (needs T µs)
CTS (echoes T)
N overhears CTS
N stays silent for T µs
Sees the CTS → close to the receiver → must stay silent for the stated duration.
Sees only the RTS, not the CTS → far from the receiver → free to transmit.

## Slide 46
802.11 · COLLISION AVOIDANCE
ACKs and Backoff
Part 7 — Wireless Networks: 802.11
Data Link Layer
46
Added by MACAW: the receiver sends an ACK after successfully receiving a frame — all nearby nodes wait for it before trying to transmit.
802.11 has no collision detection over radio — a node can’t reliably listen while it transmits.
So if two nodes’ RTS frames collide, each simply notices the missing CTS after a timeout.
Each then backs off a random amount of time — using the same exponential-backoff idea as Ethernet.

## Slide 47
802.11 · DISTRIBUTION SYSTEM
Access Points and Roaming Infrastructure
Part 7 — Wireless Networks: 802.11
Data Link Layer
47
Some nodes are Access Points (APs) — wired into a shared distribution system. Every mobile client associates itself with one AP.
distribution system
AP-1
AP-2
AP-3
A
E
A → AP-1 → (distribution system) → AP-3 → E
Even though A and E could never reach each other directly, each just needs to reach its own AP — the distribution system (a layer-2 network of its own) does the rest.

## Slide 48
802.11 · DISTRIBUTION SYSTEM
Roaming Between Access Points
Part 7 — Wireless Networks: 802.11
Data Link Layer
48
As a client moves, it may prefer a different AP — selecting one is called scanning.
Probe
Probe Response
Association Request
Association Response
Active scanning: client sends Probe frames itself, then associates with the best reply.
Passive scanning: client instead listens for periodic Beacon frames each AP broadcasts, and associates directly.
Whenever a client picks up a new AP, that new AP notifies the old one via the distribution system — the mechanism that lets a laptop or phone roam a building without dropping its link.

## Slide 49
WIRELESS NETWORKS
Beyond Wi-Fi: Bluetooth and ZigBee
Part 7 — Wireless Networks: 802.11
Data Link Layer
49
Both trade Wi-Fi’s range and bandwidth for lower power and lower cost — they solve a different problem: short-range links between nearby personal or embedded devices.
Bluetooth
2.45 GHz license-exempt band, range ≈ 10 m — a Personal Area Network (PAN)
A piconet: one master device plus up to seven slaves
Slaves talk only to the master, never to each other
An idle slave can be "parked" in a low-power state
Phones, headsets, wearables — low power, short hops
ZigBee (802.15.4)
Designed for very low bandwidth and very low power — long battery life is the priority
Simpler and cheaper than Bluetooth to embed in low-cost devices
e.g. a wall switch talking wirelessly to a ceiling fan
Embedded / always-on devices, not personal gadgets

## Slide 50
CHAPTER SUMMARY
The Chapter's Five Problems and Their Solutions
Part 7 — Wireless Networks: 802.11
Data Link Layer
50
Problem
Solution
Example
Encoding
Turn bits into a signal that survives long runs and stays clock-synchronized
Manchester encoding in classic Ethernet
Framing
Mark or count where one frame ends and the next begins
HDLC bit stuffing, PPP flag bytes
Error detection
Add redundant bits so the receiver can tell if damage occurred
CRC-32 in Ethernet and Wi-Fi
Reliable delivery
ACKs, timeouts, and a sliding window keep resending lost frames without starving the link
Stop-and-wait → sliding-window ARQ
Media access
Coordinate who gets to transmit on a shared medium
CSMA/CD (Ethernet), RTS/CTS (802.11)

## Slide 51
CHAPTER 6 · CLOSING
Recurring Themes
Boundaries, Not Just Bits
Encoding, framing, error detection, ARQ — every mechanism here answers the same question that reappears at every layer above it: where does one unit of information end, and how do we know it arrived intact?
Trust, but Verify
CRCs, checksums, and ACK/timeout pairs are all the same idea in different clothes: never assume the wire behaved — check.
Shared Media Need Etiquette
CSMA/CD and RTS/CTS solve the same "who gets to talk" problem for two very different physical worlds — a wire you can fully hear, and air you can only partly hear.
COMING UP: THE PHYSICAL LAYER
Chapter Summary
Data Link Layer
51

## Slide 52
PREVIEW — A QUICK LOOK AHEAD
Chapter 7: The Physical Layer
Not a full treatment — just the four ideas that set up everything above them.
Transmission media
Guided media (copper, fiber) that confine a signal, versus unguided media (radio, infrared) that radiate through space.
Circuit vs. packet switching
A dedicated path reserved for a call, versus store-and-forward packets sharing the same links.
The Nyquist limit
For a noiseless channel: max rate = 2H · log₂V — bandwidth and signal levels alone bound throughput.
The Shannon limit
For a noisy channel: max rate = H · log₂(1 + S/N) — the same bound this chapter opened with, now named in full.
NEXT — CHAPTER 7: THE PHYSICAL LAYER
Chapter Summary
Data Link Layer
52