## Slide 1
COMPUTER NETWORKS · CHAPTER 5 · PART II
The Internet Protocol & Routing
How IP glues a patchwork of independent networks into one — and how routers, each talking only to its neighbors, find a path across it.
A condensed, illustrated edition for lecture use

## Slide 2
01
Internetworking with IP
Gluing a patchwork of independent networks into one
Part 1 — Internetworking with IP
IP & Routing
2

## Slide 3
INTERNETWORKING WITH IP
What Is an Internetwork?
Part 1 — Internetworking with IP
IP & Routing
3
An arbitrary collection of networks interconnected —
  to provide host-to-host packet delivery across all of them
Each piece can be a completely different technology —
  an Ethernet, a point-to-point link, a wireless LAN — IP doesn’t care
Routers (R) sit at the boundaries, forwarding packets between networks —
  hosts (H) sit at the edges, only ever sending and receiving
Network 1 · Ethernet
H
H
Network 2 · Point-to-Point
H
H
Network 3 · Wireless LAN
H
H
R1
R2
A simple internetwork: three physical networks, two routers, several hosts — all reachable from each other.

## Slide 4
INTERNETWORKING WITH IP
What IP Does
Part 1 — Internetworking with IP
IP & Routing
4
IP = Internet Protocol —
  the key tool for building scalable, heterogeneous internetworks
Runs on every node in the collection — host and router alike
Defines the common infrastructure that lets networks built from different technologies function as one logical internetwork
APPLICATIONS
TRANSPORT
LINK LAYERS
HTTP
FTP
DNS
SMTP
TCP
UDP
Ethernet
Wi-Fi
PPP
ATM / FDDI
IP
the narrow waist — one common layer every network and every application agrees on

## Slide 5
INTERNETWORKING WITH IP
The IP Service Model: Connectionless & Best-Effort
Part 1 — Internetworking with IP
IP & Routing
5
IP’s two jobs — a delivery model, and a way to name everyone on the internetwork.
Packet Delivery Model
Connectionless — every datagram is routed independently, using only the address in its own header
Best-effort (unreliable) — IP promises only to try:
  packets can be lost
  packets can be delivered out of order
  duplicate copies can be delivered
  packets can be delayed a long time
Global Addressing
A uniform scheme to identify every host on the internetwork
Every address is globally unique
Addresses are hierarchical — a network part, then a host part
That hierarchy is what makes forwarding tables small — the subject of the next section

## Slide 6
INTERNETWORKING WITH IP
Design Bet: Why Best-Effort?
Part 1 — Internetworking with IP
IP & Routing
6
Reliability, ordering, flow control — IP deliberately leaves all of it out
That’s not a limitation. It’s a design choice: push complexity to the edges, keep the network’s core simple and fast
Every router just needs to get a packet one hop closer — it doesn’t remember it, doesn’t guarantee it, doesn’t wait for it
The endpoints — not the network — decide whether they need reliability, and build it themselves if they do
This is the same bet the Transport Layer makes explicit one layer up: UDP keeps IP’s best-effort model exactly as-is; TCP builds reliability, ordering, and flow control on top of it — at the edges, never inside the network.

## Slide 7
INTERNETWORKING WITH IP
The IP Datagram: Header at a Glance
Part 1 — Internetworking with IP
IP & Routing
7
Thirteen fields, but they fall into four jobs — grouped here by what they’re actually for.
CONTROL
Version (4b)
HLen (4b)
TOS (8b)
Total Length (16b)
FRAGMENTATION
Identification (16b)
Flags (3b)
Fragment Offset (13b)
DELIVERY
TTL (8b)
Protocol (8b)
Header Checksum (16b)
ADDRESSING
Source Address (32b)
Destination Address (32b)
Protocol is IP’s demux key — 6 routes the payload up to TCP, 17 to UDP
TTL is decremented at every hop; the datagram is discarded when it reaches 0

## Slide 8
02
Fragmentation
When a datagram is too big for the next link
Part 2 — Fragmentation
IP & Routing
8

## Slide 9
FRAGMENTATION
Why Fragmentation Happens
Part 2 — Fragmentation
IP & Routing
9
Every network technology imposes a Maximum Transmission Unit (MTU) —
  the largest frame that link can carry in one piece
Different technologies, very different limits
Network
Typical MTU
Ethernet
1500 bytes
FDDI
4500 bytes
802.11 Wi-Fi
~2300 bytes
Legacy PPP link
~500 bytes
A router forwarding onto a smaller-MTU network has exactly one option: split the datagram into fragments.

## Slide 10
FRAGMENTATION
How a Router Fragments a Datagram
Part 2 — Fragmentation
IP & Routing
10
Happens in a router, the moment it must forward a datagram onto a link whose MTU is too small
All resulting fragments carry the same Ident value — the destination uses it to group them back together
Fragments are themselves complete, self-contained datagrams — each can be forwarded, even fragmented again, independently
Datagram
4000B payload · Ident=71
arriving from FDDI (MTU 4500)
Router
Frag 1 · 1400B · Off=0 · MF=1
Frag 2 · 1400B · Off=1400 · MF=1
Frag 3 · 1200B · Off=2800 · MF=0
onto Ethernet · MTU 1500 · all fragments keep Ident=71

## Slide 11
FRAGMENTATION
Reassembly at the Destination
Part 2 — Fragmentation
IP & Routing
11
Reassembly happens exactly once — at the final destination host, never at an intermediate router
The Offset field says where each fragment’s data belongs in the original datagram
The More Fragments (MF) flag is set on every fragment except the last one
Frag 1
Frag 2
Frag 3
Destination host
Reassembled datagram · 4000B
IP does not recover a missing fragment: lose one, and the whole datagram is discarded — a higher layer must resend it.

## Slide 12
03
Addressing: From Classful to CIDR
How the address space nearly ran out — and was rescued
Part 3 — Addressing: From Classful to CIDR
IP & Routing
12

## Slide 13
ADDRESSING: FROM CLASSFUL TO CIDR
Classful Addressing & Dot Notation
Part 3 — Addressing: From Classful to CIDR
IP & Routing
13
Every IP address is globally unique and hierarchical: a network part, then a host part.
Class
Leading bits
Network bits
Host bits
Typical use
A
0
8
24
huge networks — up to ~16M hosts each
B
10
16
16
mid-size networks — up to ~65K hosts each
C
110
24
8
small networks — up to 254 hosts each
Of the ~4 billion IPv4 addresses: half are class A, a quarter class B, an eighth class C.
Dot notation
10.3.2.4 · class A
128.96.33.81 · class B
192.12.69.77 · class C

## Slide 14
ADDRESSING: FROM CLASSFUL TO CIDR
IP Forwarding: The Basic Idea
Part 3 — Addressing: From Classful to CIDR
IP & Routing
14
Every datagram carries its full destination address
Directly connected to the destination network? Forward straight to the host
Not directly connected? Forward to a router — chosen from a forwarding table mapping network number → next hop
Every host keeps a default router for anything not already in its (tiny) table
if NetworkNum(dest) == one of my interfaces:
deliver directly, over that interface
else if NetworkNum(dest) is in my forwarding table:
forward to NextHop router
else:
forward to my default router

## Slide 15
ADDRESSING: FROM CLASSFUL TO CIDR
Subnetting: Adding a Level to the Hierarchy
Part 3 — Addressing: From Classful to CIDR
IP & Routing
15
A class A or B network is often too big to run as one flat wire
Subnetting borrows bits from the host part to make a subnet part — a mask marks where the split falls
Subnets are visible only within the site; the rest of the Internet still sees one network number
Forwarding table at router R1
SubnetNumber
SubnetMask
NextHop
128.96.34.0
255.255.255.128
interface 0
directly connected
128.96.34.128
255.255.255.128
interface 1
directly connected
128.96.33.0
255.255.255.0
R2
via router
128.96.24.0
255.255.255.0
R3
via router (default)

## Slide 16
ADDRESSING: FROM CLASSFUL TO CIDR
Subnetting: The Forwarding Algorithm
Part 3 — Addressing: From Classful to CIDR
IP & Routing
16
D = destination IP address
for each entry <SubnetNum, SubnetMask, NextHop>:
D1 = SubnetMask & D
if D1 == SubnetNum:
if NextHop is an interface: deliver directly
else: forward to NextHop router
No match → use the default router
Mask bits need not be contiguous
Multiple subnets can share one physical wire
Subnets stay invisible from the rest of the Internet — only this site’s routers need to know the mask.

## Slide 17
ADDRESSING: FROM CLASSFUL TO CIDR
The Coming Crisis: Class B Exhaustion
Part 3 — Addressing: From Classful to CIDR
IP & Routing
17
Real networks rarely fit neatly into one of three fixed class sizes
A 2-host network forced into a class C wastes almost the whole block — 2/255 ≈ 0.8% utilized
A 256-host network forced up into a class B wastes even more — 256/65,536 ≈ 0.4% utilized
So: stop handing out class B addresses — give a growing network a bundle of class C’s instead
...except now one AS with 16 class C blocks needs 16 entries in every backbone router’s table — even though every one of them leads the same way
The cure for address exhaustion created a new disease: routing-table bloat.

## Slide 18
ADDRESSING: FROM CLASSFUL TO CIDR
The Fix: CIDR — Route Aggregation
Part 3 — Addressing: From Classful to CIDR
IP & Routing
18
Classless Inter-Domain Routing (CIDR) breaks the rigid class boundaries entirely
Hand out a contiguous block that shares a common address prefix — of any length
A single forwarding-table entry can then cover the whole block
Before — 16 class C blocks
192.4.16/24, 192.4.17/24, …, 192.4.31/24
16 separate routing-table entries
same path, every time
After — one CIDR block
192.4.16/20
same 4,096 addresses, one entry
shared top 20 bits: 11000000 00000100 0001…
The /X suffix names the prefix length in bits: 192.4.16/20 is a 20-bit prefix — between a class B (/16) and a class C (/24).

## Slide 19
ADDRESSING: FROM CLASSFUL TO CIDR
Longest-Prefix-Match Forwarding
Part 3 — Addressing: From Classful to CIDR
IP & Routing
19
CIDR means a table entry is a <prefix-length, value> pair, not a fixed-size network number
Entries can even overlap — a destination address may match more than one prefix
Rule: always forward on the most specific — the longest — matching prefix
Forwarding table at one router:
171.69/16 → path X
171.69.10/24 → path Y
Destination
Matches
Longest match used → next hop
171.69.10.5
171.69/16 and 171.69.10/24
171.69.10/24 → path Y
171.69.20.5
171.69/16 only
171.69/16 → path X

## Slide 20
04
Getting Configured: ARP, DHCP & ICMP
Three small protocols that keep the network usable
Part 4 — Getting Configured: ARP, DHCP & ICMP
IP & Routing
20

## Slide 21
GETTING CONFIGURED: ARP, DHCP & ICMP
ARP: Mapping IP to Physical Addresses
Part 4 — Getting Configured: ARP, DHCP & ICMP
IP & Routing
21
IP addresses route across the internetwork; physical (MAC) addresses deliver a frame on the local wire — something has to translate between them
ARP (Address Resolution Protocol): each host/router keeps a table of IP → physical-address bindings
Address not in the table? Broadcast a request; the target replies with its physical address
Entries are discarded if not refreshed
Host A
Host B
Host C
Host D
"Who has 10.0.0.5 ?" — broadcast from Host A, heard by every host on the wire
"10.0.0.5 is at 00:1B:63:9A" — unicast reply

## Slide 22
GETTING CONFIGURED: ARP, DHCP & ICMP
ARP in Action
Part 4 — Getting Configured: ARP, DHCP & ICMP
IP & Routing
22
Every host and router keeps a small cache of recently-resolved bindings.
IP Address
Physical Address
State
10.0.0.1
08:00:20:1A:2B:3C
fresh
default router
10.0.0.5
00:1B:63:9A:C4:11
fresh
just resolved
10.0.0.9
not cached
expired
will re-request on next use
Table-based resolution avoids encoding physical addresses inside IP addresses — a shortcut some early networks used, but one that can’t survive a change in hardware.

## Slide 23
GETTING CONFIGURED: ARP, DHCP & ICMP
DHCP: Automatic Host Configuration
Part 4 — Getting Configured: ARP, DHCP & ICMP
IP & Routing
23
Manual IP configuration doesn’t scale — tedious across a large network, and error-prone
A DHCP server holds a pool of available addresses for its administrative domain, and hands one out automatically
New host
Relay agent
(local network)
DHCP server
DHCPDISCOVER → 255.255.255.255
unicast to server
DHCPOFFER: IP + mask + default router + DNS
The reply carries everything a host needs to join the network: its IP address, subnet mask, default router, and a DNS server.

## Slide 24
GETTING CONFIGURED: ARP, DHCP & ICMP
ICMP: When Things Go Wrong
Part 4 — Getting Configured: ARP, DHCP & ICMP
IP & Routing
24
Internet Control Message Protocol — how the network reports a problem back to the source host.
Message
Meaning
Destination Unreachable
a link or node on the path has failed
Time Exceeded
TTL reached 0 — the datagram was looping
Reassembly Failed
a fragment never arrived at the destination
Parameter Problem
the IP header itself was malformed or its checksum failed
Redirect
sent router → source host: “a better route exists”
ICMP messages are themselves just best-effort IP datagrams — they can be lost too.

## Slide 25
05
Routing: Link State
How routers build a map of the whole network
Part 5 — Routing: Link State
IP & Routing
25

## Slide 26
ROUTING: LINK STATE
RIP, Briefly
Part 5 — Routing: Link State
IP & Routing
26
RIP (Routing Information Protocol) — the simplest widely-deployed distance-vector protocol
Each router periodically tells its neighbors its entire routing table — “here’s my best cost to every destination I know”
A RIPv2 packet is just a list of (destination, metric) pairs
You saw the distance-vector mechanism in depth in Part I of this chapter — RIP is exactly that algorithm, running on real routers
Simple, but slow to converge and prone to counting-to-infinity when a link fails

## Slide 27
ROUTING: LINK STATE
Link State: The Big Idea
Part 5 — Routing: Link State
IP & Routing
27
A different strategy: tell everyone — not just your neighbors — about your directly connected links
Flood that information across the whole network
Every router ends up with a full map, and computes shortest paths on its own
Distance Vector
Tells neighbors everything it knows
Talks only to directly connected neighbors
Ends up knowing just the next hop
Link State
Tells everyone just its own links
Floods to the entire network
Ends up knowing the whole map

## Slide 28
ROUTING: LINK STATE
The Link State Packet (LSP)
Part 5 — Routing: Link State
IP & Routing
28
Each router builds one small packet describing itself, and floods it
LSP {
NodeID // who created this LSP
SeqNo // increases with each new LSP
TTL // counts down; discard at 0
[(Neighbor, Cost), ...]
}
SEQNO lets routers tell “newer” from “stale” — it restarts at 0 on reboot
TTL counts down as the LSP sits in storage — old information eventually expires and is discarded

## Slide 29
ROUTING: LINK STATE
Reliable Flooding
Part 5 — Routing: Link State
IP & Routing
29
Store the most recent LSP received from each node
Forward it out every link except the one it just arrived on
Generate a new LSP periodically, incrementing SEQNO
X
A
C
B
step 1: X floods to A, C
Amber = step 1 (X → A, C) · Blue = step 2 (A, C → B — not back to X)
Every LSP reaches every router exactly once — no spanning tree needs to be computed in advance.

## Slide 30
ROUTING: LINK STATE
Dijkstra’s Algorithm
Part 5 — Routing: Link State
IP & Routing
30
Once a router has every LSP, it has the whole graph — and can compute shortest paths itself
M = {s} // nodes settled so far
for each n != s: C(n) = cost(s, n) // direct cost, ∞ if no link
while M != N:
w = node in N-M with minimum C(w)
M = M ∪ {w}
for each neighbor n of w in N-M:
C(n) = min( C(n), C(w) + cost(w, n) )
s is the router running the algorithm; each pass settles the closest unsettled node — a greedy algorithm

## Slide 31
ROUTING: LINK STATE
Worked Example: Shortest-Path Tree from A
Part 5 — Routing: Link State
IP & Routing
31
Gray lines are links (with cost). Amber arrows are the shortest-path tree Dijkstra builds from A. Each node shows its final cost from A.
2
5
1
4
1
3
1
5
2
A
0
C
3
E
5
B
2
D
4
F
7
Tree edges: A–B(2), B–C(1), C–D(1), D–E(1), E–F(2) — A–C and B–D and D–F exist but aren’t on the shortest-path tree

## Slide 32
ROUTING: LINK STATE
OSPF: Link State in Practice
Part 5 — Routing: Link State
IP & Routing
32
OSPF (Open Shortest Path First) — the link-state protocol actually deployed across the Internet’s interior
Each router runs Dijkstra locally, over the LSPs it has collected — OSPF calls them Link State Advertisements (LSAs)
Adds what a real, large network needs on top of the math:
  authentication, so a router can’t be tricked by a forged LSA
  load-balancing across multiple equal-cost paths
  hierarchical “areas”, to bound how far any one flood has to travel
The math is Dijkstra’s; everything else in OSPF exists to make flooding and computation survive a real, large, occasionally-hostile network.

## Slide 33
06
Ad Hoc & Mobile Networks
Routing when there is no fixed topology to route on
Part 6 — Ad Hoc & Mobile Networks
IP & Routing
33

## Slide 34
AD HOC & MOBILE NETWORKS
Why Ad Hoc Routing Is Different
Part 6 — Ad Hoc & Mobile Networks
IP & Routing
34
Every routing algorithm so far assumed a topology that changes slowly, if ever
Ad hoc networks break that assumption — the routers themselves are mobile
Military vehicles on a battlefield — no infrastructure
A fleet of ships at sea — all moving, all the time
Emergency workers after an earthquake — infrastructure destroyed
People with laptops, gathered somewhere with no Wi-Fi
Topology can change every few seconds — routing has to keep up with it.

## Slide 35
AD HOC & MOBILE NETWORKS
Route Discovery: Broadcast Flooding
Part 6 — Ad Hoc & Mobile Networks
IP & Routing
35
No fixed routes exist yet, so a source floods a ROUTE REQUEST outward, hop by hop
Every node hearing it for the first time rebroadcasts it further, remembering who it heard it from
When it reaches the destination, a ROUTE REPLY traces back along that reverse path
A
B
D
C
F
G
hop 1: A’s broadcast reaches B, D
hop 2: B, D rebroadcast — reaches C, F, G
thin arrow — a reverse route a REPLY could retrace

## Slide 36
AD HOC & MOBILE NETWORKS
Route Maintenance: When a Node Fails
Part 6 — Ad Hoc & Mobile Networks
IP & Routing
36
Mobile nodes fail or move out of range constantly — routes must be repaired, not just discovered once
When an intermediate node drops out, every route that passed through it breaks
Its former neighbors detect the break and send a route error back toward whoever was using that route — which then re-runs discovery
D
G
E
(a) Before — D routes to E via G
D
G
F
E
(b) After — G fails, D reroutes via F

## Slide 37
CHAPTER SUMMARY
The Protocols We Covered
Chapter Summary
IP & Routing
37
Protocol
Problem It Solves
Key Idea
IP
Deliver packets across heterogeneous networks
Connectionless, best-effort, hierarchical addressing
Fragmentation
A datagram is bigger than the next link’s MTU
Router splits it; only the destination reassembles
CIDR
Address exhaustion & routing-table growth
Variable-length prefixes + longest-prefix-match
ARP
Map an IP address to a physical (MAC) address
Broadcast a request, cache the reply
DHCP
Manual host configuration doesn’t scale
Server leases out full configuration automatically
ICMP
The network needs to report a problem
Best-effort error messages sent back to the source
Link State / OSPF
Build correct, loop-free forwarding tables
Flood link info, then run Dijkstra locally
Ad Hoc Routing
No fixed infrastructure, topology keeps changing
Discover routes on demand; repair them on failure

## Slide 38
CHAPTER 5 · PART II · CLOSING
Recurring Themes
Best-Effort, Pushed to the Edges
IP’s entire design is a bet: “best-effort in the middle, let the edges fix it” beats “guarantee everything in the middle.” Transport Layer made the same bet one layer up.
Hierarchy Tames Scale
Classful addressing, subnetting, and CIDR are all the same move: add another layer of hierarchy so a router only has to remember summaries, not every host.
Local Knowledge, Global Behavior
Link-state routers flood only what they see directly, yet every one of them computes the same global shortest-path map — order emerging from purely local information.
None of this required a single change to the applications running on top — the network layer’s job is to make heterogeneous links disappear.
NEXT — CHAPTER 6: THE DATA LINK LAYER
Chapter Closing
IP & Routing
38